## Slide 1: Speedy MINX Results
Prepared by: Elisa Dong
Feb 28, 2018

## Slide 2: Goals
Comparison for plumes retrieved by MINX and model plumes
Get useful stats in comparison
Check if current definition of plume from model is actually accurate

## Slide 3: preMINX Processing
Using AB/SK area during Sept 1-15, 2017
  Retrieved results using preMINX
    Filtered FirePixels text file using
      1. Top 10% in Power (MWatts), greater than 60% Confidence
      2. Top 20% in Power (MWatts), greater than 50% Confidence
Notes: By default, MINX only displays orbits with a certain amount of total firepower. By default, the confidence level needs to be > 40% to show up on MINX.
I left the original Fire Pixels text files alone and created new files for overlay in MINX in a separate location.
The goal of this is to reduce the total number of fires needed to be digitized and to only digitize those of interest (the two categories).

## Slide 4: Digitizing in MINX
Display customized FirePixels overlay
Select plumes based on
  Not under lots of cloud cover
  Quality: Fair or Good
  Roughly within 10km from origin
Notes: Steps:
Find plume using firepixel (red dot)
Digitize by circling the plume and providing wind direction, or drawing a line (only include parts less than ~10km away)
Check MINX results to see if the Quality: Poor (throw away if it is, or redigitize)
Results: get a bunch of plume objects

## Slide 5: postMINX Processing
Sorted red and blue band plume results
  Used the red band results if the terrain was not visible below the plume
  Otherwise used blue band results
  From MINX article, doi:10.3390/rs5094593:
    stereo retrieval coverage deteriorates dramatically as wavelength increases
    In certain cases, the greater sensitivity of the blue band to thinner aerosols allows aerosol features to be matched that correspond to a higher altitude for the plume.
    NOTE: default MINX uses both red and blue bands to image match, I picked either the blue or red band results afterwards. This should have the same effect.
speedyAltMINXdemo.py (apply to one plume)
loopSpeedMINX.py (apply to all plumes)
FST files, high resolution (for comparisons)
Produced:
  MINX plumes: colour, contour, direction, histogram, polynomial fit, scatter, shape and surface plots, basic stats (max, min, median, mean, std)
  MINX and Model plumes: colour, contour, histogram, polynomial fit, and scatter plots
  All plumes together: basic stats (total max/min, RMSD, correlation coefficient, mean bias), MINX plume and model plume comparison plot
Notes: Sorted plume results. Used the results that matched aerosol cover situation.
Wrote two scripts, one to take advantage of all the plotting functionality and treatment of plumes as objects. The other to repeat and accumulate information such as plume height and model plume height.
Low res FST files can also be compared against, just haven’t added in the AF values yet
Note that the basic stats for all the plumes has max, min. This is just a check to see that the comparison plot is correct and does not provide any other information for individual plumes.
Extra Note: Not all plots will always be produced. Since I didn’t write the postMINX program, I’m not sure why, but warnings will appear for certain plots on terminal.

## Slide 6: Sample Results – MINX Plume
Notes:   colour, contour, direction, histogram, polynomial fit, scatter, shape and surface plots, basic stats (max, min, median, mean, std)
Results: https://hpfx.science.gc.ca/~eld001/MINXResults/sept_01_15/p80_c50/thresh4/postAltOutputs/O094240-B053-SPWR01_HighRes/

## Slide 7: Sample Results – MINX and Model Plume
Notes:   MINX and Model plumes: colour, contour, histogram, polynomial fit, and scatter plots
NOTE: shape also produced, but it looks exactly the same as the one produced from the MINX plume
https://hpfx.science.gc.ca/~eld001/MINXResults/sept_01_15/p80_c50/thresh4/postAltOutputs/O094240-B053-SPWR01_HighRes/

## Slide 8: Sample Results – All Plumes
Notes: https://hpfx.science.gc.ca/~eld001/MINXResults/sept_01_15/p80_c50/thresh15/
Note to self: redo the stats for thresh4, missing the number of pairs

## Slide 9: Results for Case 1 (P90, C60)
Threshold = default = 4
  RMSD, 2720.24617395
  Correlation Coefficient, (0.11845588056825707, 0.25549033571820351)
  Mean Bias, 3176143.78634
Threshold = 15
  RMSD, 2635.61288679
  Correlation Coefficient, (-0.56235304904112915, 5.3018125518963431e-06)
  Mean Bias, 1807981.51358
  Number of Pairs, 57
Notes: Note Correlation Coefficients
Significantly better when cutting out lower values of PM2.5
https://hpfx.science.gc.ca/~eld001/MINXResults/sept_01_15/p90_c60/

## Slide 10: Results for Case 2 (P80, C50)
Threshold = default = 4
  RMSD, 2415.7960233
  Correlation Coefficient, (0.0084792036678869188, 0.90139646216419811)
  Mean Bias, 2676414.46297
Threshold = 15
  RMSD, 1867.73033029
  Correlation Coefficient, (-0.31736273589809633, 3.4625309580168156e-05)
  Mean Bias, 1214650.36139
  Number of Pairs, 164
Notes: Correlation also better when threshold is higher, but overall has gone down compared to case 1
Should probably check if it’s the percentile, or the confidence levels
https://hpfx.science.gc.ca/~eld001/MINXResults/sept_01_15/p80_c50/

## Slide 11: Blue and Red Bands
Ran additional cases
If digitizer doesn’t know how to classify red/blue
Using the same 2 conditions, threshold = 15, Processed:
  All blue band plume results
  All red band plume results
Notes: Note: It’s a little subjective as to whether or not the results should be in the blue or red band.
MINX can output both.
The following pages evaluate in the case of AB/SK during sept1-15, which band to use always if unsure how to categorize
NOTE: results may be skewed. Will have to check, but usually more plumes that should be viewed in red band.

## Slide 12: Results for Case 1 (P90, C60)
Red Band Plumes
  RMSD, 2615.38515849
  Correlation Coefficient, (-0.5601613690230256, 4.8245153034138419e-06)
  Mean Bias, 1811570.28575
  Number of Pairs, 58
Blue Band Plumes
  RMSD, 2346.52238071
  Correlation Coefficient, (-0.48455015807666041, 0.001532602190660252)
  Mean Bias, 1084959.07057
  Number of Pairs, 40
Notes: General pattern and correlation is roughly the same. This is expected since the same plumes were processed.

## Slide 13: Results for Case 2 (P80, C50)
Red Band Plumes
  RMSD, 2197.17999412
  Correlation Coefficient, (-0.36147195144609651, 6.222726409088604e-05)
  Mean Bias, 1405047.73982
  Number of Pairs, 117
Blue Band Plumes
  RMSD, 1681.96838944
  Correlation Coefficient, (-0.36208131455134307, 0.37810112306164534)
  Mean Bias, 435233.486629
  Number of Pairs, 8
Notes: Note that red band has more matches though. Ie. MINX results for blue band likely results in greater number of missing values for the plume objects.

## Slide 14: Next Steps
Do a few more cases (vary percentile and confidence, more days if available)
Incorporate observational data (from hotspots)
  Ideally find fires longer than one day
  Compare model predictions, satellite values and reported values
  Check that reported values are actually matching up to satellite values
    May find that satellite and hotspot info don’t match up, would expected model to be off as well…

## Slide 15: All Results
Link to results: https://hpfx.science.gc.ca/~eld001/MINXResults/sept_01_15/